## Slide 2: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 3: Experiment Design Goal
Goals of this project:
Evaluate ICA - Algorithms in terms of robustness
Elaborating new approaches to increase robustness against noise and outliers in EEG - measurements
Problems:
The solution of ICA is not unique: and can pertubed, scaled or have sign changes
Find metrics which deal with that
How can we evaluate the ICA-Algorithms?
The ICA-Algorithms return the reconstructed signal and an estimated mixing matrix
2 options: compare input and reconstructed signals or compare mixing matrix with its estimate

## Slide 4: Experiment Design Metrics: MD, MSE
Mean squared Error (MSE):
Taking the Mean of the squared residuals
Obtained values = number of signals take mean or median
Minimum Distance Index (based on MM):
Key idea: The inverse of the Mixing Matrix equals the Unmixing Matrix, so the multiplication is the identity matrix
Therefore: if The Algorithm performed well
Where considers Permutation P, Scaling D and sign changes J, p = number of signals
= Minimize Frobenius Norm
0 indicates a good performance, 1 indicates a bad one
residuals
Problem:
Required groundtruth data for X and W

## Slide 5: Experiment Design General approach
2. Run different Algorithms for different cases:
  different Sample Sizes,
  different levels of contamination (noise, outlier)
3. Evaluate on MD or MSE
What we did:
We generated ideal Input Signals and a random ideal Mixing Matrix. groundtruth
Standard Signals:
ECG Signal: 2Hz
Sinus: 5Hz
Rectangle: 10Hz
Sawtooth: 25Hz
fs: 1000Hz
Normalized to [-1,1]
Brainwaves [3]:
4. Do this multiple times (reproducability)
Monte Carlo Study
5. Statistical Analyses on multiple outcomes
interpret results

## Slide 6: Experiment Design Monte Carlo Flow Chart
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Standard input signals
ECG, Sinus, Rectangle, Sawtooth
3. Contaminate signals
Add single or patchy Outlier (100std) and/or white noise (40dBB)
2. Mix Signals with mixing matrix (random)
4. Whitening process
Decorrelate Signals: meaning that the sample covariance matrix is diagonal and that all the diagonal elements are equal.
5. Perform ICA
4 Algos: JADE, RADICAL, CoroICA, PowerICA
6. Evaluate single run
Minimum Distance, MSE
7. Evaluate ICA
Get 1000 MDs and MSEs.
BoxPlot

## Slide 7: Experiment Design Definition of test characteristics
1.) Focus on Sample Size
Initialize standard signals with different Sample Sizes: 1000, 2500, 5000, 10000, 15000 evaluate on 1000runs
2.) Focus on amount of noise/outlier – Breakdown Point Analyses
Initialize standard signals with fix Sample Size of 10000
N
Type I: No Noise, No Outlier
Type III: No Noise, 0.1%
Outlier(std = 100)
Type II: 40dB SNR, No Outlier
Type IV: 40dB SNR, 0.1%
Outlier (std = 100)
Type V: increase noise, SNR: 40 dB,
30 dB, 20 dB, 10 dB, 6 dB, 3 dB
Type VII: increase Outlier impulsive %: 0.1,
0.25, 0.5, 1, 1.5, 5, 10, 20, 50 (100 STD)
Type VI: increase Outlier patchy %: 0.1,
0.25, 0.5, 1, 1.5, 5, 10, 20, 50 (100 Std)
Notes: ICONS !!!

## Slide 8: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
Notes: MD not linear ..

## Slide 9: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes

## Slide 10: Results Interpreting the Minimum Distance
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes
: not all signal reconstructed, bigger spikes
Notes: MD no linear measure – see 0.4 to 0.6

## Slide 11: Experiment results Type 1
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Sample Size 10000
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE
Pros:
All Algorithms are able to reconstruct the source signals
Cons:
Radical: Long runtime unusable for real time processing
CoroICA: Only good results for tested signals by Hyperparameter tuning

## Slide 12: Experiment results Type 1 - 4
Sample Size of min. n = 5000 is necessary
Even 0.1% Outlier causes failure for every algorithm
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE
For 40dB SNR variance increases slightly, more outliers
Hop at 10000: Drawback of the MD – metric is not perfect
Next Step:
Breakdown Analyses – How much noise does it take to cause a breakdown?
Sample Size 10000

## Slide 13: Experiment results Type 5 - 7
Robust Covariance Estimation in Whitening:
Causes breakdown
Robust objective Function in higher Order statistics:
JADE: Causes breakdown
Did our robustness plugins improve the results ?
Type 6-7:
Complete breakdown even for 1 outlier
Type 5:
Noise <20dB SNR breakdown
Power ICA – Type 5: 3-40dB Noise, No Outlier
SNR (additive noise)
3.0
6.0
30.0
40.0
0.2
0.4
0.8
MD
MSE
10.0
20.0
0.6
0.0
0.2
0.6
0.4
Intermediate conclusion:
Preprocessing of the data essential! Outlier removal + smoothing
We need new approaches to improve the performance
Notes: Felix Kasten

## Slide 14: Towards EEG data Synthetic EEG artifact reconstruction
Synthetic - EEG data
3. We generated realistic artifacts and added one on each channel
Artifacts which typically come along with EEG data [Delorme2007]
Optional: Add single or patchy (100std) Outliers and white noise (3std)
1. Use standard signals as input signals
2. Mix Data with random mixing matrix
4. Performed ICA
Realistic artifacts [Delorme2007]
Muscle
Eye Blink
Electrical
Electrical
Notes: Low frequency events – modelling eye Blink artifacts around 1-3Hz
Transient high frequency events 20-60Hzmodelling muscle artifacts
Signal discontinuities from electrical artifacts
Linear trends from eletrical artifacts

## Slide 15: Towards EEG data Results with synthetic EEG data
Mixed signals + added artifacts
Reconstructed signals + artifacts
PowerICA
Able to reconstruct the standard signals and the EEG artifacts
Eye Blink
Muscle
electrical
electrical

## Slide 16: Literature
[Delorme2007] - Enhanced detection of artifacts in EEG data using higher-order statistics and independent component analysis in NIH 2007
[2] - https://mne.tools/dev/overview/datasets_index.html visited 02.16.2021
[3] - https://brainworksneurotherapy.com/what-are-brainwaves

## Slide 17: Towards EEG data Results with synthetic EEG data
Synthetic EEG artifacts
Standard Input Signals
Mixed signals + added artifacts
Reconstructed signals + artifacts
PowerICA
Able to reconstruct the standard signals and the EEG artifacts

## Slide 18: Towards EEG data Synthetic EEG artifact reconstruction
Synthetic - EEG data
3. We generated realistic artifacts and added one on each channel
Artifacts which typically come along with EEG data [Delorme2007]
Optional: Add single or patchy (1000std) Outliers and white noise (3std)
1. Use real EEG data as input signals
2. Mix Data with random mixing matrix
4. Perform ICA
EEG - data
Muscle
Eye Blink
Electrical
Electrical
Realistic artifacts [Delorme2007]
Notes: Show reconstructed artifacts

## Slide 19: Experiment Design Experiment Types
1.) Focus on Sample Size
Initialize standard signals with different Sample Sizes: 1000, 2500, 5000, 10000, 15000
    Type I: No Noise, No Outlier, 1000 runs
    Type II: 40dB SNR, No Outlier, 1000 runs
    Type III: No Noise, 0.1% Outlier with std = 100, 1000 runs
    Type IV: 40dB SNR, 0.1% Outlier with std = 100, 1000 runs
2.) Focus on amount of noise/outlier – Breakdown Point Analyses
Initialize standard signals with fix Sample Size of 10000
    Type V: increase noise SNR: 40 dB, 30 dB, 20 dB, 10 dB, 6 dB, 3 dB
    Type VI: increase Outlier patchy %: 0.1, 0.25, 0.5, 1, 1.5, 5, 10, 20, 50 with 100 STD
    Type VII: increase Outlier impulsive %: 0.1, 0.25, 0.5, 1, 1.5, 5, 10, 20, 50 with 100 STD
N
N
Notes: ICONS !!!

## Slide 20: Results Type 5 - 7
Robust Covariance Estimation in Whitening:
Causes breakdown
Robust objective Function in higher Order statistics:
JADE: Causes breakdown
Did our Robustness Plugins improve the results ?
Type 6-7:
Complete breakdown even for 1 outlier
Type 5:
Noise <20dB SNR breakdown
Conclusion:
Preprocessing of the data essential! -> Outlier removal + Smoothing (e.g Low pass Filtering)
We need new approaches to improve the performance

## Slide 21: Minimum Distance
MD of 0 -> good, MD->1 bad, Optimum = Identity, Only possible if Ground truth
availavble

## Slide 22: Results Type 1 - 4
Sample Size of min. n = 5000 is neccessary
Even 0.1% Outlier causes failure for every algorithm
For 40dB SNR -> variance increses slightly, more outliers
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
Power ICA
Next Step:
How much noise does it take to cause a breakdown ?

## Slide 23: MSE, SNR
Evaluate for every single signal

## Slide 24
Delorme one slide -> near eeg, closer to reality
2. cases -> classical rosbustness
-> eeg like artifacts
Good and bad recon
Signal to Noise Ratio (SNR):
Considered here as the variance of the resiudal
Transformed in dB
4 values take mean or median
Possible Reasons:
Distributions don‘t follow the expected model
Important values are weighted down by new objective functions
Matrix fett schreiben
Eventuelle andere Signale zeigen auf slide 1
4 Signale ersetzen
Drop bei 10000 erklären -> auf drawbacks von MD hinweisen.
Evtl auch nur bis 5000 zeigen

## Slide 25: Experiment Design Monte Carlo Flow Chart III
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
How do we measure the performance of the Algorithms ?
1. Evaluation on Metrics:
= recovered Signals, = estimated Mixing Matrix
Evaluate the performance each run
Based on Mixing Matrix: Minimum Distance:
Based on reconstructed Signals: Mean squared error: ), Signal to Noise Ratio: )
2. Empirical Data Analyses
Get 1000 (#runs) metrics
Calcualte: Mean, Standard Deviation, Median, nMAD of MD,MSE,SNR
BoxPlot
vs.

## Slide 26: Experiment Design Monte Carlo Flow Chart II
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Independent Component Analyses
Whitening
Plug in robustness
Perform Robust Covariance Estimation from Python Package RobustSP
Spatial Median
M-Estimator of Scatter Matrix (Huber)
Perform ICA by 4 different Algorithms: JADE, RADICAL, CoroICA, PowerICA
Plug in Robustness JADE: Replace Expected Value by robust objective function.
Huber, Tukey

## Slide 27: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
MD = 0.2