## Slide 1: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 2: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard Power ICA (1000 samples)
Input signals
Power ICA
Graph Power ICA

## Slide 3: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard Power ICA (1000 samples)
0,4
0,19
0,1
0,6
0,1
0,6
Power ICA
Graph Power ICA
MD
MSE

## Slide 4: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)
Graph Power ICA
Power ICA
Input signals

## Slide 5: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)
0,38
0,2
0,8
Power ICA
Graph Power ICA
0,2
0,8
MSE
MD

## Slide 6: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)
Input signals
Graph Power ICA
Power ICA

## Slide 7: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)
0,8
0,4
0,4
1,4
MSE
MD
1,0
Power ICA
Graph Power ICA

## Slide 8: Towards EEG data Synthetic EEG artifact reconstruction
Semi-synthetic EEG data:
3. We generated realistic artifacts and added one on each channel
Artifacts which typically come along with EEG data [Delorme2006]
Optional: Add single or patchy (1000std) Outliers and white noise (3std)
1. Use real EEG data as input signals
2. Mix Data with random mixing matrix
4. Perform Power ICA and Graph Power ICA
EEG data:
Muscle
Eye Blink
Electrical
Electrical
Synthetic EEG artifacts:
Notes: Show reconstructed artifacts

## Slide 9: Graph BSS Results Semi-synthetic EEG data
Muscle
Eye Blink
Electrical
Electrical
Noise
0
1
2
3
4
5
6
0
1
2
3
4
5
6
t[s]
t[s]
Artifacts clearly extractable:
Power ICA
EEG artifacts

## Slide 10: Graph BSS Results Semi-synthetic EEG data
Also possible with Graph Power ICA:
0
1
2
3
4
5
6
t[s]
Graph Power ICA
0
1
2
3
4
5
6
t[s]
Power ICA

## Slide 11: Graph BSS Results Semi-synthetic EEG data
Events clearly extractable:
Button push
Visual stimulus
Power ICA
0
1
2
3
4
5
6
t[s]

## Slide 12: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 13: Summary of major outcomes
Question 1: What is ICA?
Question 2: How to compare algorithms?
Question 3: Which algorithm performs best? What happens with noise or outlier?
Question 4: How to robustify algorithms?
Question 5: What is Graph Signal processing / Graph BSS?
Question 6: Outcomes of Graph Signal processing?

## Slide 14: Summary of major outcomes Question 1: What is ICA?
  Mathematical concept to extract (independent = non-gaussian) signals from mixed signals
  Different approaches to obtain the demixing matrix  4 algorithms
  „ICA tries to decorrelate mixed up signals and find the optimal demixing matrix based on optimizing different measures of independence“
CoroICA

## Slide 15: Summary of major outcomes Question 2: How to compare algorithms?
  Minimum distance, MSE and SNR
  Correlation of different metrics important
  „One Metric sometimes provides not the whole information: We need to find how different metrics correlate“
0,0
0,8
0,2
0,4
0,6
0,0
0,8
0,2
0,4
0,6
1,0
Median of MSEs
Minimum Distance
0,4
0,19
0,1
0,6
Power ICA
Graph Power ICA
MD

## Slide 16: Summary of major outcomes Question 3: Which algorithm performs best? What happens with noise or outlier?
  Monte Carlo run with 10.000 runs: Evaluate metrics
    More or less similar with good data (simulated and real EEG data with added artifacts)
    Power ICA: quite good with reasonable SNR (~ 20dB), fast and with low variance
    Low sample sizes are problematic (< 5000 samples)
    Higher noise than 20dB SNR: smoothly becoming worse
    All reach breakdown point with one large outlier
  „All four algorithms: Good performance on well behaving data but higher noise level or larger outlier cause
  failure  Violates assumptions“
Notes: Low sample size problematisch: central limit theorem  finite variance (ausreißer macht infinite variance)
Gaussian noise (gegen die Annnahmen von ICA)
Ergebnisse machen Sinn: Annahmen über ICA
Robustness nicht gegeben, da asymptotisches Verhalten verändert
Assumptions sagen!
iid, finite covariance, dürfen nicht Gauss sein

## Slide 17: Summary of major outcomes Question 4: How to robustify?
  Whitening process crucial for algorithms
  Different objective functions for some algorithms
  Initialization quite important (local maxima/minima)
  Within algorithms: quite complicated  model based
  What we tried:
    Plug-in robustness of covariance estimation in whitening process
    Trying out different robust objective functions
    Initialize Power ICA with Radical as a global optimizer
  „No real improvement: sometimes with noise a bit better, but still low
  breakdown point”
Notes: Robust whitening: probem mit outlier
Problem mit outlier: Unterschied non-Gaussian signals und non-Gaussian outlier
Annahmen verletzen -> ist sinnvoll das es nicht funktioniert
=> Model gibt es nícht her

## Slide 18: Summary of major outcomes Question 5: What are Graph Signals / Graph BSS?
  Graph signal: Use proximity/similarity between components of the underlying signal
  „Graph BSS tries to combine the ICA approach to maximize the measure of independence and the graph signal approach to decorrelate the nodes of the graph”
1
N
0
2
3
…
Notes: - Wir haben uns damit beschäftigt!

## Slide 19: Summary of major outcomes Question 6: Outcomes of Graph BSS?
  Monte Carlo with 1000 runs:
    Better Blind Source Separation with good signals (low sample size)
    Similar with noisy data
    Breakdown point with one outlier as well
    Problem with graph structure
„Graph BSS is good for low sample sizes and if the graph structure is available. Otherwise similar outcomes as standard BSS”
Real EEG data with artifacts separable!
Notes: - ICA vesagt: also versagt auch Graph BSS

## Slide 20: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 21: Problems and future research
Problems:
Low Breakdown point
High noise dependency
Sample size important for standard ICA
Graph structure estimation: How to find correlation of graph signals?
Covariance estimation in higher dimensions problematic
Time consumption for real time EEG analysis
Future research:
Robust whitening / preprocessing (Robust covariance estimation in high dimensions)
Incorporate noise process and outlier in model for ICA algorithm
Find good graph structure estimation (recent research [Garcia2020])
Notes: Defusion based vs decorrelation based (-> time and spatial )
- New Outlier & non-Gaussianity measure finden

## Slide 22: Thank you for your attention!

## Slide 23: Sources
Delorme et al.: “Enhanced detection of artifacts in EEG data using higher-order statistics and independent component analysis”, Elsevier 2006
Garcia et al.: ”Blind Demixing of Diffused Graph Signals”, arXiv 2020