## Slide 1: Spatial Filtering for Source Separation in EEG Data
Christian Endl, Felix Wirth, Korbinian Kunst & Taulant Koka

## Slide 2: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 3: Motivation Challenge of Working with EEG Data
What do we get in experiments?
“
Working with EEG data is
therefore the process of source separation
EEG Channels
time t in seconds
What we wish to have?
Electroencephalogram (EEG) Concept
We are observing the "oscillating slow fields" of neurons in the upper layers of the cerebral cortex.
These changes in electrical potential lead a neuron to be more likely or less likely to fire action potentials and are important in encoding information in the brain.
Notes: The feature extraction of ICA was motivated by neurosciences that suggest that the similar principle of redundancy reduction explains some aspects of the early processing of sensory data by the brain.

## Slide 4: Spatial Filtering for Source Separation Cocktail Party Problem
Def. II: The topic of separating mixed sources is called Blind Source Separation (BSS) and can be solved by algorithms called Independent Component Analysis (ICA).
Def. I: In contrast to temporal filtering in DSP where a signal is analyzed as time-(in)variant subsequent discrete values of one channel, spatial filtering looks at the relation of a given timepoint across multiple channels.
Notes: Sosund is particular good example because sound add linearly

## Slide 5: The Concept of Source Separation Cocktail Party Problem

## Slide 6: The Concept of Source Separation Cocktail Party Problem

## Slide 7: The Concept of Source Separation Cocktail Party Problem

## Slide 8: The Concept of Source Separation Cocktail Party Problem
Sensors
Reconstructed Signals
Original Signals (Sources)
Latent Variables
Observed Data
Result of the ICA

## Slide 9: The Concept of Source Separation Cocktail Party Problem
Sensors
Latent Variables
Observed Data
Overlay of Signals
Mixing Matrix
Original Signals (Sources)

## Slide 10: The Concept of Source Separation Math Formulation for ICA (Independent Component Analysis)
x
s
W
matrix of vector mixtures is generated by
is the unobserved matrix of statistically independent components (IC)
is the unknown mixing matrix of full rank, whose coefficient represents the contribution of the -th source onto -th mixture.
he parameter of interest, defined by the inverse of the mixing matrix, called the demixing matrix and its (transposed) -th row vector is called the -th demixing vector.
fundamental assumption of ICA is that the data is a linear mixture of statistically independent sources

## Slide 11: Independent Component Analysis Solving blind source seperation using ICA
What is the goal of the algorithm?
Find the demixing matrix so that the latent source variable s can be reconstructed as by the observed data
Under-constrained problem: unknown and focus on finding based on underlying statistics of X
Don’t solve for W all in one: step wise
Remember SVD? a rotation a stretch along the axes , and a second rotation .
How can the the Independent Components be interpreted?
How can we find W based on X?
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture
Find two unknowns A and s by only obersving theier matrix product x, underconstrained problem,
Amplitudes
Unsupervised learning problem

## Slide 12: Independent Component Analysis Solving blind source seperation using ICA
If we can find each of the SVD components we can determine the unmixing matrix A
It can be shown that this can be formulated as an eigenvector problem, where:
=
D, E are the singular values and eigenvectors composed from the covariance matrix of X
decorrelation
normalization
After this Process which is called whitening we ware left with a distribution where all second order correlations are removed:
Problem simplified to finding:
need to exploit the statistics of independence to identify V
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture
Projection the data onto the principal components aka aligning with cartesian coordinates removes linear correlation
Normalizes variance in each direction by multiplying with d^-0.5 => all dimensions are expressed in standard units
V measure of dipendency

## Slide 13: Notes On ICA Assumptions
Components of the covariance matrix 􏰳{xxH} − 􏰳{x}􏰳{x}H are second order cumu
lants. The higher order cumulants of x can be considered as a measure of the gap t
o Gaussianity since they are zero when variable x is normal.

## Slide 14: Notes On ICA Assumptions
Central limit theorem: two non gaussian distributions overlayed will be more gaussian than a single one
Meaning: multiple non gaussian distributions tend to form a gaussian distributions
That means: a gaussian disitribution can also be decorrelated two non-gaussian distribution again
How can we measure non-gaussianity?
Can also be shown on mutial information (paper verweis, gaussian ist intuitiver, mutial information leads to cleaner mathematical proove
Why is it possible?
What are general assumptions for ICA?
Sources are statistical independent & non gaussian
Mixture of signals is linear
Number of Sensors >= Number of Sources
Large sample size of signals
Soures are stationary
Observed signals are zero mean

## Slide 15: Independent Component Analysis A generic Algorithm description
Rotate the data such that either
  (a) the output signal components are as statistically independent as possible
  (b) the output signal components are most non-Gaussian.
1. Subtract off the mean of the data in each dimension.
2. Whiten the data by calculating the eigenvectors of the co-variance of the data.
3. Identify final rotation matrix that optimizes statistical independence.
Quick Summary of the Algorithm:
What is left to compute:
ICA Algorithms – a broad overview:
Notes: Measure for non gaussianity: kurtossis measure for statistically independent Kullback Leibler
Central limit theorem: overlay

## Slide 16: Independent Component Analysis Example Concept PowerICA
La Grangian Optimiziation Problem for find rotation matrix V
non-Gaussianity measure
unit-norm constraint
can be any twice continuously differentiable nonlinear and non-quadratic function
is Lagrange Multiplier
itself is found via a stepwise Newton Raphson optimization algorithm
local maxima

## Slide 17: ICA Signal Reconstruction From Mixed Example Signals to Deconstructed Signals
ECG
Rectangle
Saw
Sin

## Slide 18: Independent Component Analysis Notes on peculiarities of ICA
Original Signals
Reconstructred signal Signals
Due to ambiguities of the method the extracting of the unobserved independent source signals is only accurate up to:
𝑑 × 𝑑 permutation matrix , scaling matrix and sign-change matrix
Permutation
Permutation
Sign Change
Scaling
Notes: P = (obtained by permuting the rows of 𝑑 × 𝑑 identity matrix),
D = (a diagonal matrix with positive diagonal elements)

## Slide 19: Notes On ICA Back – Up Slide I:
Signal Processing Technique of extracting unobserved independent source signals from their observed multivariate mixture recordings
don’t solve for W all in one: step wise