## Slide 2: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 3: Experiment Design Goal
Goals of this project:
Evaluate ICA - Algorithms in terms of robustness
Elaborating new approaches to increase robustness against noise and outliers in EEG - measurements
Problems:
The solution of ICA is not unique: and can pertubed, scaled or have sign changes
Find metrics which deal with that
How can we evaluate the ICA-Algorithms?
The ICA-Algorithms return the reconstructed signal and an estimated mixing matrix
2 options: compare input and reconstructed signals or compare mixing matrix with its estimate

## Slide 4: Experiment Design Metrics: MD, MSE
Mean squared Error (MSE):
Taking the Mean of the squared residuals
Obtained values = number of signals take mean or median
Minimum Distance Index (based on MM):
Key idea: The inverse of the Mixing Matrix equals the Unmixing Matrix, so the multiplication is the identity matrix
Therefore: if The Algorithm performed well
Where considers Permutation P, Scaling D and sign changes J, p = number of signals
= Minimize Frobenius Norm
0 indicates a good performance, 1 indicates a bad one
residuals
Problem:
Required groundtruth data for X and W

## Slide 5: Experiment Design General approach
What we did:
We generated ideal Input Signals and a random Mixing Matrix. groundtruth
ECG Signal: 2Hz
Sinus: 5Hz
Rectangle: 10Hz
Sawtooth: 25Hz
fs: 1000Hz
Normalized to [-1,1]
From us defined Standard Signals
Frequencies of Brainwaves [3]:
=
Groundtruth mixing matrix

## Slide 6: Experiment Design Monte Carlo Flow Chart
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Standard input signals
ECG, Sinus, Rectangle, Sawtooth
3. Contaminate signals
Add single or patchy Outlier (100std) and/or white noise (40dB)
2. Mix Signals with mixing matrix (random)
4. Whitening process
Decorrelate Signals: meaning that the sample covariance matrix is diagonal and that all the diagonal elements are equal.
5. Perform ICA
4 Algos: JADE, RADICAL, CoroICA, PowerICA
6. Evaluate single run
Minimum Distance, MSE
7. Evaluate ICA
Get 1000 MDs and MSEs.
BoxPlot

## Slide 7: Experiment Design Definition of test characteristics
1.) Focus on Sample Size
Initialize standard signals with different Sample Sizes: 1000, 2500, 5000, 10000, 15000 evaluate on 1000runs
2.) Focus on amount of noise – Breakdown Analyses
Initialize standard signals with fix Sample Size of 10000
N
Type I: No Noise, No Outlier
Type III: No Noise, 0.1%
Outlier(std = 100)
Type II: 40dB SNR, No Outlier
Type IV: 40dB SNR,
0.1% Outlier (std = 100)
Type V: increase noise, SNR: 40 dB,
30 dB, 20 dB, 10 dB, 6 dB, 3 dB
Notes: ICONS !!!

## Slide 8: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
Notes: MD not linear ..

## Slide 9: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes

## Slide 10: Results Interpreting the Minimum Distance
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes
: not all signal reconstructed, bigger spikes
Notes: MD no linear measure – see 0.4 to 0.6

## Slide 11: Experiment results Type 1
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Sample Size 10000
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE
Pros:
All Algorithms are able to reconstruct the source signals
Cons:
Radical: Long runtime unusable for real time processing
CoroICA: Only good results for tested signals by Hyperparameter tuning
Notes: Explain Plot, Examplarly plotted PowerICA here,
MD and Mse are going down for higher samples sizes
All Algorithms were good in the ideal case, shown here are the MDs and MSEs for all algorithms
And now we look on type 1-4

## Slide 12: Experiment results Type 1 - 4
Sample Size of min. n = 5000 is necessary
For 40dB SNR variance increases slightly, more outliers
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE
Even 0.1% Outlier causes failure for every algorithm
Hop at 10000: Drawback of the MD – metric is not perfect
Next Step:
Breakdown Analyses – How much noise does it take to cause a breakdown?
Sample Size 10000

## Slide 13: Experiment results Type 5
Robust Covariance Estimation in Whitening:
Could not prevent breakdown
Occasionally causes breakdown
Robust objective Function in higher Order statistics:
Could not prevent breakdown
Occasionally causes breakdown
Did our robustness plugins improve the results ?
Type 5:
Noise < 20dB SNR breakdown
Power ICA – Type 5: 3-40dB Noise, No Outlier
SNR (additive noise)
3.0
6.0
30.0
40.0
0.2
0.4
0.8
MD
MSE
10.0
20.0
0.6
0.0
0.2
0.6
0.4
Intermediate conclusion:
Pre-processing of the data essential! Outlier removal + smoothing
We need new approaches to improve the performance
Notes: We decreased SNR from 40dB to 3db …

## Slide 14: Literature
[Delorme2007] - Enhanced detection of artifacts in EEG data using higher-order statistics and independent component analysis in NIH 2007
[2] - https://mne.tools/dev/overview/datasets_index.html visited 02.16.2021
[3] - https://brainworksneurotherapy.com/what-are-brainwaves

## Slide 15: Towards EEG data Synthetic EEG artifact reconstruction
Synthetic - EEG data
3. We generated realistic artifacts and added one on each channel
Artifacts which typically come along with EEG data [Delorme2007]
Optional: Add single or patchy (100std) Outliers and white noise (3std)
1. Use standard signals as input signals
2. Mix Data with random mixing matrix
4. Performed ICA
Realistic artifacts [Delorme2007]
Muscle
Eye Blink
Electrical
Electrical
Notes: Low frequency events – modelling eye Blink artifacts around 1-3Hz
Transient high frequency events 20-60Hzmodelling muscle artifacts
Signal discontinuities from electrical artifacts
Linear trends from eletrical artifacts

## Slide 16: Towards EEG data Results with synthetic EEG data
Mixed signals + added artifacts
Reconstructed signals + artifacts
PowerICA
Able to reconstruct the standard signals and the EEG artifacts
Eye Blink
Muscle
electrical
electrical

## Slide 17: Minimum Distance
MD of 0 -> good, MD->1 bad, Optimum = Identity, Only possible if Groundtruth
available

## Slide 18: Results Type 1 - 4
Sample Size of min. n = 5000 is neccessary
Even 0.1% Outlier causes failure for every algorithm
For 40dB SNR -> variance increses slightly, more outliers
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
Power ICA
Next Step:
How much noise does it take to cause a breakdown ?

## Slide 19: MSE, SNR
Evaluate for every single signal