## Slide 1: Spatial Filtering for Source Separation in EEG Data
Christian Endl, Felix Wirth, Korbinian Kunst & Taulant Koka

## Slide 2: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 3: Motivation Challenge of Working with EEG Data
What do we get in experiments?
“
Working with EEG data is
therefore the process of source separation
EEG Channels
time t in seconds
What we wish to have?
Electroencephalogram (EEG) Concept
We are observing the "oscillating slow fields" of neurons in the upper layers of the cerebral cortex.
These changes in electrical potential lead a neuron to be more likely or less likely to fire action potentials and are important in encoding information in the brain.

## Slide 4: Spatial Filtering for Source Separation Cocktail Party Problem
Def. II: The topic of separating mixed sources is called Blind Source Separation (BSS) and can be solved by algorithms called Independent Component Analysis (ICA).
Def. I: In contrast to temporal filtering in DSP where a signal is analyzed as time-(in)variant subsequent discrete values of one channel, spatial filtering looks at the relation of a given timepoint across multiple channels.
Notes: Sosund is particular good example because sound add linearly

## Slide 5: The Concept of Source Seperation Cocktail Party Problem

## Slide 6: The Concept of Source Seperation Cocktail Party Problem

## Slide 7: The Concept of Source Separation Cocktail Party Problem
Sensors
Reconstructed Signals
Original Signals
Latent Variables
Observed Data
Result of the ICA

## Slide 8: The Concept of Source Separation Cocktail Party Problem
Sensors
Original Signals
Latent Variables
Observed Data
Overlay of Signals
Mixing Matrix

## Slide 9: The Concept of Source Separation Math Formulation for ICA (Independent Component Analysis)
x
s
W
matrix of vector mixtures is generated by
is the unobserved matrix of statistically independent components (IC)
is the unknown mixing matrix of full rank, whose coefficient represents the contribution of the -th source onto -th mixture.
he parameter of interest, defined by the inverse of the mixing matrix, called the demixing matrix and its (transposed) -th row vector is called the -th demixing vector.

## Slide 10: Independent Component Analysis Solving blind source seperation using ICA
What is the goal of the algorithm?
Find the demixing matrix so that the latent source variable s can be reconstructed as by the observed data
Under-constrained problem: unknown and focus on finding based on underlying statistics of X
Don’t solve for W all in one: step wise
Remember SVD? a rotation a stretch along the axes , and a second rotation .
How can the the Independent Components be interpreted?
How can we find W based on X?
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture

## Slide 11: Independent Component Analysis Solving blind source seperation using ICA
If we can find each of the SVD components we can determine the unmixing matrix A
It can be shown that this can be formulated as an eigenvector problem, where:
=
D, E are the singular values and eigenvectors composed from the covariance matrix of X
decorrelation
normalization
After this Process which is called whitening we ware left with a distribution where all second order correlations are removed:
Problem simplified to finding:
need to exploit the statistics of independence to identify V.
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture

## Slide 12: Independent Component Analysis A generic Algorithm description
Rotate the data such that either
  (a) the output signal components are as statistically independent as possible
  (b) the output signal components are most non-Gaussian.
1. Subtract off the mean of the data in each dimension.
2. Whiten the data by calculating the eigenvectors of the co-variance of the data.
3. Identify final rotation matrix that optimizes statistical independence.
Quick Summary of the Algorithm:
What is left to compute:
ICA Algorithms – a broad overview:

## Slide 13: Independent Component Analysis Example Concept PowerICA
LaGrangian Optimiziation Problem for find rotation matrix V
non-Gaussianity measure
unit-norm constraint
can be any twice continuously differentiable nonlinear and non-quadratic function
is Lagrange Multiplier
itself is found via a stepwise Newton Raphson optimization algorithm
local maxima

## Slide 14: Independent Component Analysis Example Algorithm PowerICA – alternative approach up for discussion
unit-norm constraint
non-Gaussianity measure
Verbalize this!

## Slide 15: ICA Signal Reconstruction From Mixed Example Signals to Deconstructed Signals
ECG
Rectangle
Saw
Sin

## Slide 16: Independent Component Analysis Notes on peculiarities of ICA
Original Signals
Reconstructred signal Signals
Due to ambiguities of the method the extracting of the unobserved independent source signals is only accurate up to:
𝑑 × 𝑑 permutation matrix , scaling matrix and sign-change matrix
Permutation
Permutation
Sign Change
Scaling
Notes: P = (obtained by permuting the rows of 𝑑 × 𝑑 identity matrix),
D = (a diagonal matrix with positive diagonal elements)

## Slide 17: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 18: Experiment Design Goal
Goals of this project:
Evaluate ICA -Algorithms in terms of robustness
Elaborating new approaches to increase robustness against noise and outliers in EEG-measurements
Problems:
The solution of ICA is not unique: and can pertubed, scaled or have sign changes
Find Metrics which deal with that
How can we evaluate the ICA-Algorithms?
The ICA-Algorithms return the reconstructed Signal and an estimated Mixing Matrix
2 options: compare Input and Reconstructed Signals or Compare Mixing Matrix A with its estimate

## Slide 19: Experiment Design Metrics: MD, MSE
Mean squared Error (MSE):
Taking the Mean of the squared residuals
4 values take mean or median
Minimum Distance Index (based on MM):
Key idea: The inverse of the Mixing Matrix equals the Unmixing Matrix, so the multiplication is the identity matrix
Therefore: if The Algorithm performed well
Where considers Permutation P, Scaling D and sign changes J, p = number of signals
= Minimize Frobenius Norm
0 indicates a good performance, 1 indicates a bad one
residuals
Problem:
Required groundtruth data for X and A

## Slide 20: Experiment Design General approach
2. Run different Algorithms for different cases:
  different Sample Sizes,
  different levels of contamination (noise, outlier)
3. Evaluate on MD, MSE, SNR
What do we have to do:
Generate ideal Input Signals and a random ideal Mixing Matrix. groundtruth
Standard Signals:
ECG Signal: 2Hz
Sinus: 5Hz
Rectangle: 10Hz
Sawtooth: 25Hz
fs: 1000Hz
Normalized to [-1,1]
Brainwaves:
4. Do this multiple times (reproducability)
Monte Carlo Study (random Input, deterministic output)
5. Statistical Analyses on multiple outcomes
interpret results

## Slide 21: Experiment Design Monte Carlo Flow Chart
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Standard Input Signals
ECG, Sinus, Rectangle, Sawtooth
3. Contaminate Signals
Add single or patchy Outlier (1000std) and/or white noise (3std)
2. Mix Signals with Mixing Matrix A (random)
4. Whitening Process
Decorrelate Signals: meaning that the covariance matrix is diagonal and that all the diagonal elements are equal.
5. Perform ICA
4 Algos: JADE, RADICAL, CoroICA, PowerICA
6. Evaluate Single Run
Minimum Distance, MSE
7. Evaluate ICA
Get 1000 MDs and MSEs.
BoxPlot

## Slide 22: Experiment Design Expirement Types
1.) Focus on Sample Size
Initialize standard signals with different Sample Sizes: 1000, 2500, 5000, 10000, 15000
Type I: No Noise, No Outlier, 1000 runs
Type II: 40dB SNR, No Outlier, 1000 runs
Type III: No Noise, 0.1% Outlier with std = 100, 1000 runs
Type IV: 40dB SNR, 0.1% Outlier with std = 100, 1000 runs
2.) Focus on amount of noise/outlier
Initialize standard signals with fix Sample Size of 10000
Type V: increase noise SNR: 40 dB, 30 dB, 20 dB, 10 dB, 6 dB, 3 dB
Type VI: increase Outlier patchy %: 0.1, 0.25, 0.5, 1, 1.5, 5, 10, 20, 50 with 1000 STD
Type VII: increase Outlier impulsive %: 0.1, 0.25, 0.5, 1, 1.5, 5, 10, 20, 50 with 1000 STD
Type VIII: increase Outlier amount = 1, with 3, 10, 50, 100, 1000 STD

## Slide 23: Results Type 1 - 4
MD = 0.6
MD = 0.4
MD = 0.2

## Slide 24: Results Type 1 - 4
Type 1 (ideal) | Median MD | Median MSE | Median SNR [dB]
PowerICA |  |  | 
Jade |  |  | 
CoroICA |  |  | 
Radical |  |  | 
Type 1 (ideal) | Median MD | Median MSE | Median SNR [dB]
PowerICA |  |  | 
Jade |  |  | 
CoroICA |  |  | 
Radical |  |  | 
Sample Size 10000

## Slide 25: Results Type 1 - 4
Sample Size of min. n = 5000 is neccessary
Even 0.1% Outlier causes failure for every algorithm
For 40dB SNR -> variance increses slightly, more outliers
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
PowerICA | Median MD | Median MSE | Median SNR [dB]
Type 1 (ideal) |  |  | 
Type 2 (noise) |  |  | 
Type 3 (outlier) |  |  | 
Type 4 (noise + outlier) |  |  | 
Power ICA
Next Step:
How much noise does it take to cause a breakdown ?

## Slide 26: Results Type 5 - 7
Robust Covariance Estimation in Whitening:
Causes breakdown
Robust objective Function in higher Order statistics:
JADE: Causes breakdown
Did our Robustness Plugins improve the results ?
Type 6-7:
Complete breakdown even for 1 outlier
Type 5:
Noise <20dB SNR breakdown
Conclusion:
Preprocessing of the data essential! -> Outlier removal + Smoothing
We need new approaches to improve the performance
Power ICA

## Slide 27: EEG case study Semi Synthetic EEG data as Input Signals
Semi Synthetic electroencephalogram - EEG data
3. Add 1 realistic artifact, on mixed data
Optional: Add single or patchy Outliers and white noise (3std)
Artifacts which typically come along with EEG data
Muscle
Eye Blink
Electrical
Electrical
1. Use real EEG data as Inputs
Insert Plot here
2. Mix Data with random Mixing Matrix

## Slide 28: EEG case study Results with Semi Synthetic EEG data
Able to reconstruct the EEG signals and Artifacts
Insert Plot here

## Slide 29: TODO
Delorme one slide -> near eeg, closer to reality
2. cases -> classical rosbustness
-> eeg like artifacts
Good and bad recon
Signal to Noise Ratio (SNR):
Considered here as the variance of the resiudal
Transformed in dB
4 values take mean or median
Possible Reasons:
Distributions don‘t follow the expected model
Important values are weighted down by new objective functions
Matrix fett schreiben
Eventuelle andere Signale zeigen auf slide 1
4 Signale ersetzen
Drop bei 10000 erklären -> auf drawbacks von MD hinweisen.
Evtl auch nur bis 5000 zeigen

## Slide 30: Experiment Design Monte Carlo Flow Chart III
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
How do we measure the performance of the Algorithms ?
1. Evaluation on Metrics:
= recovered Signals, = estimated Mixing Matrix
Evaluate the performance each run
Based on Mixing Matrix: Minimum Distance:
Based on reconstructed Signals: Mean squared error: ), Signal to Noise Ratio: )
2. Empirical Data Analyses
Get 1000 (#runs) metrics
Calcualte: Mean, Standard Deviation, Median, nMAD of MD,MSE,SNR
BoxPlot
vs.

## Slide 31: Experiment Design Monte Carlo Flow Chart II
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Independent Component Analyses
Whitening
Plug in robustness
Perform Robust Covariance Estimation from Python Package RobustSP
Spatial Median
M-Estimator of Scatter Matrix (Huber)
Perform ICA by 4 different Algorithms: JADE, RADICAL, CoroICA, PowerICA
Plug in Robustness JADE: Replace Expected Value by robust objective function.
Huber, Tukey

## Slide 32: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 33: Shortcomings
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one Gaussian signal
For SNR ≤ 20dB high variance in performance
    Failures become increasingly likely
Inherently unrobust against outliers
    A single outlier will lead to failure of the method
3. SNR ≤ 20dB
2. Gaussian
4. Outlier
1. Samples
N

## Slide 34: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory
In 2020: First approaches to combine non-gaussianity based BSS with graph-based BSS (Jari Miettinen)
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)

## Slide 35: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory
In 2020: First approaches to combine non-gaussianity based BSS with graph-based BSS (Jari Miettinen)
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)
  Information about underlying graph structure
Combine those in a way that they complement each other

## Slide 36: Graph Blind Source Separation
What are Graphs?

## Slide 37: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
Edges represent proximity between two vertices
Graph structure can be stored in a matrix ⇒ The adjacency matrix A
Examples: Social networks, sensor networks, brain networks, etc.
7
2
5
4
6
1
3
Undirected unweighted graph
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
A =

## Slide 38: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
Edges represent proximity between two vertices
Graph structure can be stored in a matrix ⇒ The adjacency matrix A
Examples: Social networks, sensor networks, brain networks, etc.
7
2
5
4
6
1
3
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
A =
Undirected unweighted graph

## Slide 39: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Each node represents a sample point
Directed graph ⇒ unsymmetric adjacency
1
N
0
2
3
…
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
A =
1 0 0 0 0 0 … 0
. . . . . . … 0
n ∈ ℕ, n ≤ N

## Slide 40: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Multiple Signals can share the same graph
In this case: The class of all periodic signals with period N
1
N
0
2
3
…
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
A =
1 0 0 0 0 0 … 0
. . . . . . … 0
n ∈ ℕ, n ≤ N

## Slide 41: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
We call a graph-shift by k
  For Line Graph ⇔ Shift operator as known from Digital Signal Processing
When a graph-shift is applied, the signal will shift along every connected path made up of the k nearest edges.
1
N
0
2
3
…
k = 1 shift
n ∈ ℕ, n ≤ N

## Slide 42: Graph Blind Source Separation Graph-Autocorrelation
Using the introduced graph-shift we define the graph-autocorrelation matrix analog to the sample autocorrelation:
N dimensional square matrix of sample autocorrelation
N dimensional square matrix of graph-autocorrelation for k graph-shifts
k-th power of Adjacency matrix corresponding to k shifts along the graph
D signals stored as column vectors
The k-shift along paths of an underlying graph can provide additional information about independence between signals!
,
: Identity Matrix

## Slide 43: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
Find a matrix that diagonalizes as much as possible
The solution for decorrelates the signals in the graph-sense
  is a solution of the BSS problem for graph-signals
N

## Slide 44: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
N
PowerICA shortcomings:
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one gaussian signal
Graph based BSS and non-gaussianity based BSS seem to make up for each others weak points.

## Slide 45: Graph Blind Source Separation Composite Objective
Composite objective function
How can we combine them?
Approach from Jari Miettinen et al. (Aalto University)
Define composite objective function :
PowerICA objective:
Maximize estimate of negentropy as a measure of non-Gaussianity with the Lagrangian method.
Graph decorrelation objective:
Diagonalize graph-autocorrelation as much as possible. For only one adjacency ⇒ eigenvalue problem.
+
Balance Parameter

## Slide 46: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 47: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard PowerICA (1000 samples)

## Slide 48: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard PowerICA (1000 samples)
0,4
0,19
0,1
0,6
0,1
0,6

## Slide 49: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)

## Slide 50: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)
0,38
0,2
0,8
0,2
0,8

## Slide 51: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)

## Slide 52: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)
0,8
0,4
1,4
0,4
1,4

## Slide 53: Graph BSS Results
Also possible for semi-synthetic EEG data
0
1
2
3
4
5
6
0
1
2
3
4
5
6
t[s]
t[s]

## Slide 54: Graph BSS Results Semi-synthetic EEG data
Artifacts clearly extractable:

## Slide 55: Graph BSS Results Semi-synthetic EEG data
Events clearly extractable:
Button push
Visual stimulus
0
1
2
3
4
5
6
t[s]

## Slide 56: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 57: Summary of major outcomes
Question 1: What is ICA?
Question 2: How to compare algorithms?
Question 3: Which algorithm performs best? What happens with noise or outlier?
Question 4: How to robustify algorithms?
Question 5: What is Graph Signal processing / Graph BSS?
Question 6: Outcomes of Graph Signal processing?

## Slide 58: Summary of major outcomes Question 1: What is ICA?
  Mathematical concept to extract (independent = non-gaussian) signals from mixed signals
  Different approaches to obtain the demixing matrix  4 algorithms
  „ICA tries to decorrelate mixed up signals and find the optimal demixing matrix based on optimizing different measures of independence“
CoroICA

## Slide 59: Summary of major outcomes Question 2: How to compare algorithms?
  Minimum distance, MSE and SNR
  Correlation of different metrics important
  „One Metric sometimes provides not
  the whole information: We need to find
  how different metrics correlate“
0,0
0,8
0,2
0,4
0,6
0,0
0,8
0,2
0,4
0,6
0,0
0,8
0,2
0,4
0,6
1,0
0,0
0,8
0,2
0,4
0,6
1,0
Median of MSEs
Mean of MSEs
Minimum Distance
Minimum Distance
0,4
0,19
0,6
0,1

## Slide 60: Summary of major outcomes Question 3: Which algorithm performs best? What happens with noise or outlier?
  Monte Carlo run with 10.000 runs: Evaluate metrics
    More or less similar with good data (simulated (stationary) and real EEG data with added artifacts (non-stationary))
    PowerICA: quite good with reasonable SNR (~20dB), fast and with low variance
    Low sample sizes are problematic (<5000 samples)
    Higher noise than 20dB SNR: smoothly becoming worse
    All reach breakdown point with one large outlier
  „All four algorithms: Good performance on well behaving data but higher noise level or larger outlier cause
  failure  No real robust algorithm“

## Slide 61: Summary of major outcomes Question 4: How to robustify?
  Whitening process crucial for algorithms
  Different objective functions for some algorithms
  Initialization quite important (local maxima/minima)
  Within algorithms: quite complicated  model based
  What we tried:
    Plug-in robustness of covariance estimation in whitening process
    Trying out different robust objective functions
    Initialize PowerICA with Radical as a global optimizer
  „No real improvement: sometimes with noise a bit better, but still low
  breakdown point”

## Slide 62: Summary of major outcomes Question 5: What is Graph Signal processing / Graph BSS?
  Graph signal processing: Use proximity/similarity between components of the underlying signal
  „Graph BSS tries to combine the ICA approach to maximize the measure of independence and the graph signal approach to decorrelate the nodes of the graph”
1
N
0
2
3
…

## Slide 63: Summary of major outcomes Question 6: Outcomes of Graph BSS?
  Monte Carlo with 1000 runs:
    Better Blind Source Separation with good signals (low sample size)
    Real EEG data with artifacts separable
    Similar with noisy data
    Breakdown point with one outlier as well
    Problem with graph structure
„Graph BSS is good for low sample sizes and if the graph structure is available. Otherwise similar outcomes as standard BSS”

## Slide 64: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 65: Problems and future research
Problems:
Low Breakdown point
High noise dependency
Sample size important for standard ICA
Graph structure estimation: How to find correlation of graph signals?
Covariance estimation in higher dimensions problematic
Time consumption for real time EEG analysis
Future research:
Robust whitening / preprocessing
Incorporate noise process and outlier in model for ICA algorithm
Find good graph structure estimation
Robust covariance estimation in high dimensions

## Slide 66: Thank you for your attention!