## Slide 1: Spatial Filtering for Source Separation in EEG Data
Christian Endl, Felix Wirth, Korbinian Kunst & Taulant Koka

## Slide 2: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 3: Motivation Challenge of Working with EEG Data
What do we get in experiments?
“
Working with EEG data is
therefore the process of source separation
EEG Channels
time t in seconds
What we wish to have?
Electroencephalogram (EEG) Concept
We are observing the "oscillating slow fields" of neurons in the upper layers of the cerebral cortex.
These changes in electrical potential lead a neuron to be more likely or less likely to fire action potentials and are important in encoding information in the brain.
[NY Times, 2020]
[BackyardBrains]
Notes: The feature extraction of ICA was motivated by neurosciences that suggest that the similar principle of redundancy reduction explains some aspects of the early processing of sensory data by the brain.

## Slide 4: Spatial Filtering for Source Separation Cocktail Party Problem
Def. II: The topic of separating mixed sources is called Blind Source Separation (BSS) and can be solved by algorithms called Independent Component Analysis (ICA).
Def. I: In contrast to temporal filtering in DSP where a signal is analyzed as time-(in)variant subsequent discrete values of one channel, spatial filtering looks at the relation of a given timepoint across multiple channels.
iStock
Notes: Sosund is particular good example because sound add linearly

## Slide 5: The Concept of Source Separation Cocktail Party Problem

## Slide 6: The Concept of Source Separation Cocktail Party Problem

## Slide 7: The Concept of Source Separation Cocktail Party Problem

## Slide 8: The Concept of Source Separation Cocktail Party Problem
Sensors
Reconstructed Signals
Original Signals (Sources)
Latent Variables
Observed Data
Result of the ICA

## Slide 9: The Concept of Source Separation Cocktail Party Problem
Sensors
Latent Variables
Observed Data
Overlay of Signals
Mixing Matrix
Original Signals (Sources)

## Slide 10: The Concept of Source Separation Math Formulation for ICA (Independent Component Analysis)
S
X
S
W
matrix of vector mixtures is generated by
is the unobserved matrix of statistically independent components (IC)
is the unknown mixing matrix of full rank, whose coefficient represents the contribution of the -th source onto -th mixture.
he parameter of interest, defined by the inverse of the mixing matrix, called the demixing matrix and its (transposed) -th row vector is called the -th demixing vector.

## Slide 11: Independent Component Analysis Solving blind source seperation using ICA
What is the goal of the algorithm?
Find the demixing matrix so that the latent source variable S can be reconstructed as by the observed data
Under-constrained problem: unknown and focus on finding based on underlying statistics of X
Don’t solve for all in one: step wise
Remember Singular Value Decomposition (SVD) ? Every symmetric matrix can be decomposed into a rotation a stretch along the axes , and a second rotation .
How can we find W based on X?
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture
Find two unknowns A and s by only obersving theier matrix product x, underconstrained problem,
Amplitudes
Unsupervised learning problem

## Slide 12: Independent Component Analysis Solving blind source seperation using ICA
If we can find each of the SVD components we can determine the unmixing matrix A
It can be shown that this can be formulated as an eigenvector problem, where:
=
D, E are the singular values and eigenvectors computed from the covariance matrix of X ()
decorrelation
normalization
After this Process which is called whitening we ware left with a distribution where all second order correlations are removed [Shlens, 2010]:
Problem simplified to finding:
need to exploit the statistics of independence to identify V
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture
Projection the data onto the principal components aka aligning with cartesian coordinates removes linear correlation
Normalizes variance in each direction by multiplying with d^-0.5 => all dimensions are expressed in standard units
V measure of dipendency

## Slide 13: Notes On ICA Assumptions
Central limit theorem: two non gaussian distributions overlayed will be more gaussian than one
  Meaning: multiple non gaussian distributions tend to form a gaussian distributions
  We can use this: a gaussian distribution can also be decorrelated two non-gaussian distribution again
How can we measure non-gaussianity ?
  Kurtosis, Entropy and measures derived from this [Hyvarinen, 2000]
Why is it possible?
What are general assumptions for ICA?
Sources are statistical independent & non gaussian for identifiability of the model [Comon, 1994]
Mixture of signals is linear [Shlens, 2010]
Number of Sensors Number of Sources [C. Jutten, 2010]
Large sample size of signals
Sources are stationary [C. Jutten, 2010]
Observed signals are zero mean [C. Jutten, 2010]
How to measure statistical independence?
For ICA There are two main approaches [Haykin, 2009] [Hyvarinen, 2000]: a) rooted minimization of mutual information b) maximization of non-Gaussianity
Notes: Can also be shown on mutial information (paper verweis, gaussian ist intuitiver, mutial information leads to cleaner mathematical proove
ICA estimation by minimization of mutual information is equivalent to maximizing the sum of non-Gaussianities of the estimates, when the esti- mates are constrained to be uncorrelated.

## Slide 14: Independent Component Analysis A generic Algorithm description
1. Subtract off the mean of the data in each dimension.
2. Whiten the data by calculating the eigenvectors of the co-variance of the data.
3. Identify final rotation matrix that optimizes statistical independence
  Contribution of ICA algo: formulate a contrast function that measures how close the estimated sources are to statistical independence
  Reach goal by minimizing or maximizing defined objective
Quick Summary of the Algorithm:
ICA Algorithms – a subjective selective overview:
[Sejnowski TJ , 1995] ]
[Miettinen, 2020]
[Pfister 2019]
[Hyvärinen, 1999]
[Basiri, 2017 ]
[Sejnowski TJ , 1995]
[Cardoso 1993 ]
[Learned-Miller, 2003]
Notes: Measure for non gaussianity: kurtossis measure for statistically independent Kullback Leibler
Central limit theorem: overlay

## Slide 15: Independent Component Analysis Example Concept PowerICA [Basiri, 2017]
LaGrangian optimiziation problem for find rotation matrix V
non-Gaussianity measure
unit-norm constraint
can be any twice continuously differentiable nonlinear and non-quadratic function
  or [Hyvärinen, 1999]
is Lagrange Multiplier
itself is found via a stepwise Newton Raphson optimization algorithm
local maxima

## Slide 16: ICA Signal Reconstruction From Mixed Example Signals to Deconstructed Signals
ECG
Rectangle
Saw
Sin

## Slide 17: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 18: Experiment Design Goal
Goals of this project:
Evaluate ICA - Algorithms in terms of robustness
Elaborating new approaches to increase robustness against noise and outliers in EEG - measurements
Problems:
The solution of ICA is not unique: and can pertubed, scaled or have sign changes
Find metrics which deal with that
How can we evaluate the ICA-Algorithms?
The ICA-Algorithms return the reconstructed signal and an estimated mixing matrix
2 options: compare input and reconstructed signals or compare mixing matrix with its estimate

## Slide 19: Experiment Design Metrics: MD, MSE
Mean squared Error (MSE):
Taking the Mean of the squared residuals
Obtained values = number of signals take mean or median
Minimum Distance Index (based on MM):
Key idea: The inverse of the Mixing Matrix equals the Unmixing Matrix, so the multiplication is the identity matrix
Therefore: if The Algorithm performed well
Where considers Permutation P, Scaling D and sign changes J, p = number of signals
= Minimize Frobenius Norm
0 indicates a good performance, 1 indicates a bad one
residuals
Problem:
Required groundtruth data for X and W

## Slide 20: Experiment Design General approach
What we did:
We generated ideal Input Signals and a random Mixing Matrix. groundtruth
ECG Signal: 2Hz
Sinus: 5Hz
Rectangle: 10Hz
Sawtooth: 25Hz
fs: 1000Hz
Normalized to [-1,1]
From us defined Standard Signals
Frequencies of Brainwaves
[Koudelková2018] :
=
Groundtruth mixing matrix

## Slide 21: Experiment Design Monte Carlo Flow Chart
Input Signals
Mix Signals
Contaminate Signals
Whitening
ICA
Evaluate on Metrics
Empirical Data Analyses
Runs = 1000
Standard input signals
ECG, Sinus, Rectangle, Sawtooth
3. Contaminate signals
Add single or patchy Outlier (100std) and/or white noise (40dB)
2. Mix Signals with mixing matrix (random)
4. Whitening process
Decorrelate Signals: meaning that the sample covariance matrix is diagonal and that all the diagonal elements are equal.
5. Perform ICA
4 Algos: JADE, RADICAL, CoroICA, PowerICA
6. Evaluate single run
Minimum Distance, MSE
7. Evaluate ICA
Get 1000 MDs and MSEs.
BoxPlot

## Slide 22: Experiment Design Definition of test characteristics
1.) Focus on Sample Size
Initialize standard signals with different Sample Sizes: 1000, 2500, 5000, 10000, 15000 evaluate on 1000runs
2.) Focus on amount of noise – Breakdown Analyses
Initialize standard signals with fix Sample Size of 10000
N
Type I: No Noise, No Outlier
Type III: No Noise,
0.1% Outlier(std = 100)
Type II: 40dB SNR, No Outlier
Type IV: 40dB SNR,
0.1% Outlier (std = 100)
Type V: increase noise, SNR: 40 dB,
30 dB, 20 dB, 10 dB, 6 dB, 3 dB
Notes: ICONS !!!

## Slide 23: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
Notes: MD not linear ..

## Slide 24: Results Interpreting the Minimum Distance
MD = 0.6
MD = 0.4
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes

## Slide 25: Results Interpreting the Minimum Distance
: Good results, small spikes, some sign changes
: signals are recognizable, bigger spikes
: not all signal reconstructed, bigger spikes
Notes: MD no linear measure – see 0.4 to 0.6

## Slide 26: Experiment results Type 1
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Type 1 (ideal) | Median MD | Median MSE
PowerICA |  | 
Jade |  | 
CoroICA |  | 
Radical |  | 
Sample Size 10000
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE
Pros:
All Algorithms are able to reconstruct the source signals
Cons:
Radical: Long runtime unusable for real time processing
CoroICA: Only good results for tested signals by Hyperparameter tuning
Notes: Explain Plot, Examplarly plotted PowerICA here,
MD and Mse are going down for higher samples sizes
All Algorithms were good in the ideal case, shown here are the MDs and MSEs for all algorithms
And now we look on type 1-4

## Slide 27: Experiment results Type 1 - 4
Sample Size of min. n = 5000 is necessary
For 40dB SNR variance increases slightly, more outliers
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
PowerICA | Median MD | Median MSE
Type 1 (ideal) |  | 
Type 2 (noise) |  | 
Type 3 (outlier) |  | 
Type 4 (noise + outlier) |  | 
Even 0.1% Outlier causes failure for every algorithm
Hop at 10000: Drawback of the MD – metric is not perfect
Next Step:
Breakdown Analyses – How much noise does it take to cause a breakdown?
Sample Size 10000
PowerICA – Type 1: No Noise, No Outlier
Sample Size
1000
2500
5000
10000
15000
0.0
0.1
0.2
0.2
0.4
0.6
MD
MSE

## Slide 28: Experiment results Type 5
Robust Covariance Estimation in Whitening:
Could not prevent breakdown
Occasionally causes breakdown
Robust objective Function in higher Order statistics:
Could not prevent breakdown
Occasionally causes breakdown
Did our robustness plugins improve the results ?
Type 5:
Noise < 20dB SNR breakdown
Power ICA – Type 5: 3-40dB Noise, No Outlier
SNR (additive noise)
3.0
6.0
30.0
40.0
0.2
0.4
0.8
MD
MSE
10.0
20.0
0.6
0.0
0.2
0.6
0.4
Intermediate conclusion:
Pre-processing of the data essential! Outlier removal + smoothing
We need new approaches to improve the performance
Notes: We decreased SNR from 40dB to 3db …

## Slide 29: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 30: Shortcomings
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one Gaussian signal
For SNR ≤ 20dB high variance in performance
    Failures become increasingly likely
Inherently unrobust against outliers
    A single outlier will lead to failure of the method
3. SNR ≤ 20dB
2. Gaussian
4. Outlier
1. Samples
N
Notes: As Korbinian pointed out:
  we observe several deficits of the method ,which are cloesly related to the assumptions we made for ICA in general
  1. The Algorithm struggled with low numbers of observations of the signals, needed at least 5000 to perform well consistently
  2. can’t recover more than one gaussian signal
  3. If SNR < 20dB, the number of failures increases
  4. Early Breakdown for a single outlier already
Raises the Question: What other approaches to ICA are there?

## Slide 31: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory [Blöchl, 2010]
In 2020: First approaches to combine non-Gaussianity based BSS with graph based BSS (Jari Miettinen et al.) [Miettinen, 2020]
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)
Notes: In 2010 a research team from Helmholtz Research Center came up with a method to use graph theory based Signal Separation
10 years later - > Aalto research group around Esa Ollila and Jari Miettinen came up with an approach to combine this graph based Method with non-Gaussianity based ICA by:
  Maximizing some Non-Gaussianity measure and

## Slide 32: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory [Blöchl, 2010]
In 2020: First approaches to combine non-Gaussianity based BSS with graph based BSS (Jari Miettinen et al.) [Miettinen, 2020]
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)
  Information about underlying graph structure
Combine those in a way that they complement each other
Notes: In 2010 a research team from Helmholtz Research Center came up with a method to use graph theory based Signal Separation
10 years later - > Aalto research group around Esa Ollila and Jari Miettinen came up with an approach to combine this graph based Method with non-Gaussianity based ICA by:
  Using some Non-Gaussianity measure and information about some network topology
At first this sounds very appealing, but one might ask: What are graphs?

## Slide 33: Graph Blind Source Separation What are Graphs?
Notes: In following: A short introduction to the concepts we used

## Slide 34: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
Edges represent proximity between two vertices
Graph structure can be stored in a matrix ⇒ The adjacency matrix A [Djuric, 2018]
Examples: Social networks, sensor networks, brain networks, etc.
7
2
5
4
6
1
3
Undirected unweighted graph
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
=
Notes: Firs of all: A set of vertices/nodes that is connected by some edges is called a Graph
  The edges represent some kind of proximity ore closeness of the nodes
  Example Facebook/Instagram: Each member is a vertex, each friendship or follower is an edge
  Edges may be directed or undirected
    Undirected: If I am friends with Korbinian or Felix on Facebook, it means they are also friends with me => the friendship is mutual)
    Directed: If I follow someone on Instagram it doesn’t mean they necessarily follow me to
  This information about the topology of the graph can be stored compactly in an adjacency matrix

## Slide 35: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
The Entry represents the edge between node i and j
7
2
5
4
6
1
3
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
=
Undirected unweighted graph
Notes: each i,jth entry of the Adjacency matrix represents the edge between nodes i and j and A_ji the edge between j and i
If node 1 is representing me and node 7 is representing Korbinian it would mean that we are friends, or that we are both following each other or some other kind of mutual connection

## Slide 36: Graph Blind Source Separation Graph Signals
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Each node represents a sample point
Directed graph ⇒ unsymmetric adjacency [Djuric, 2018]
1
N
0
2
3
…
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
=
1 0 0 0 0 0 … 0
. . . . . . … 0
n ∈ ℕ, n ≤ N
Notes: Now that we know Graphs, we can introduce the concept of Signals on this graph
Actually we already know one => the time axis in discrete time signals can be represented as Line graph, in the case of periodic signals it woul be a recursive or cyclic line graph as shown here
This graph is directed (because flow of time is directed) => leads to A unsymmetric
In this representation each node of the Graph represents a time instance of the Signal

## Slide 37: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Multiple Signals can share the same graph
In this case: The class of all periodic signals with period N [Djuric, 2018]
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
=
1 0 0 0 0 0 … 0
. . . . . . … 0
1
N
0
2
3
…
n ∈ ℕ, n ≤ N
Notes: Examples of corresponding edges in the Adjacency matrix are depicted in colors ( green to last node, orange to first node)
It is important to note, that there can be various signals that share the same graph structure
In this case that would be : all periodic signals with Period of length N
Now that we have established what graph signals are, we can go ahead and define the Graph Shift

## Slide 38: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
We call a graph shift by k
  For Line Graph ⇔ Shift operator as known from Digital Signal Processing
When a graph shift is applied, the signal will shift along every connected path made up of the k nearest edges. [Djuric, 2018]
1
N
0
2
3
…
n ∈ ℕ, n ≤ N
k = 1 shift
Notes: Graph Shift analog to the Shift Operator known from Digital Signal Processing:
  In fact it is the same, for this type of Line Graph
This Propagation of the Signal through the graph, can be achieved by multiplication of the Signals X with the Adjacency Matrix A^k , where k is the length of the shift
So we can state that graph shift by k will propagate the signal along every connected path along the k nearest outgoing edges
Let‘s see what would happen, if we had an edge going from node 0 to node 3

## Slide 39: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
We call a graph shift by k
  For Line Graph ⇔ Shift operator as known from Digital Signal Processing
When a graph shift is applied, the signal will shift along every connected path made up of the k nearest edges. [Djuric, 2018]
1
N
0
2
3
…
n ∈ ℕ, n ≤ N
k = 1 shift
Notes: As you can see, having additional connections between nodes will lead to a linear combination of the values of the signal that have been propagated through the incident edges into a node
In this case we have added up the values shifted from node 0 and node 2 into node 3
With all of this we are now able to define the Graph autocorrelation

## Slide 40: Graph Blind Source Separation Graph Autocorrelation
Using the introduced graph shift we define the graph autocorrelation matrix analog to the sample autocorrelation [Blöchl, 2010] :
D dimensional square matrix of sample autocorrelation
D dimensional square matrix of graph autocorrelation for k graph-shifts
k-th power of adjacency matrix corresponding to k shifts along the graph
D signals stored as column vectors
The k-shift along paths of an underlying graph can provide additional information about the source signals!
,
: Identity Matrix
Notes: Analog to the sample autocorrelation matrix, which equals the sample covariance matrix because we have centered our data beforehand to have zero mean
We can define the graph autocorrelation as the correlation between the Signals X and the signals X at a lag k, meaning that it has been shifted by k through the graph
With that in mind it is easy to see that for k = 0 our Shift Operator will be equal to the Identity matrix and we end up with the sample autocorrelation matrix ,
This shift through the Graph, provides us with additional information about our sources, if they follow some other order than just the line-graph
Having this additional Information, we can use a decorrelation method to seperate our signals

## Slide 41: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
Find a matrix that diagonalizes as much as possible [Blöchl, 2010]
The solution for decorrelates the signals in the graph-sense
  is an estimate for the solution of the BSS problem for graph-signals
N
Notes: That, we do by finding a matrix W which diagonalizes our graph autocorrelation as much possible
In all of this we asssume whitened data
Then, W is an estimate for the Solution of the Source Separation Problem
This Method, has some noteworthy advantages:
  Unlike ICA it does not presume any specific distribution of the signals, meaning it works with gaussian signals as well
  The sample sizes can be much lower, (performs well with 1000 samples already)
  There are numerous underlying network topologies in real world problems
However, these graph structures are most of the time not directly available and need to be inferred by some method
Therefore it is a major disadvantage, that the performance of the algorithm is highly dependent on accurate graph estimations

## Slide 42: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
N
PowerICA shortcomings:
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one Gaussian signal
Graph based BSS and non-Gaussianity based BSS seem to make up for each others weak points.
Notes: Comparing this with the shortcomings of PowerICA adressed earlier it seems that they complement each other
So the Question is, how do we combine them?

## Slide 43: Graph Blind Source Seperation Composite Objective
Composite objective function
How can we combine them?
Approach from Jari Miettinen et al. (Aalto University) [Miettinen, 2020]
Define composite objective function :
PowerICA objective:
Maximize estimate of non-Gaussianity with the Lagrangian method.
Graph decorrelation objective:
Diagonalize graph autocorrelation matrix(matrices) as much as possible. For only one adjacency ⇒ eigenvalue problem.
+
Balance Parameter
Notes: The approach by Jari Miettinens group at Aalto considers first the two objective functions of
  An ICA objective, which we chose to be PowerICA, that tries to separate the signals by maximizing non-Gaussianity
  The Graph decorrelation objective, which is the diagonalization process of the graph autocorrelation
We cannot simply add them up as they are, but by introducing a new parameter lambda, that balances the two objective functions, we arrive at the composite objective function
And how this concept fared, you will hear by Christian

## Slide 44: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 45: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard Power ICA (1000 samples)
Input signals
Power ICA
Graph Power ICA

## Slide 46: Graph BSS Results Clean data
Standard signals (Cos, Rect, ECG, Saw)
Clean data: Better results than standard Power ICA (1000 samples)
0,4
0,19
0,1
0,6
0,1
0,6
Power ICA
Graph Power ICA
MD
MSE

## Slide 47: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)
Graph Power ICA
Power ICA
Input signals

## Slide 48: Graph BSS Results Noisy data
Comparable for noisy signals (up to 20dB SNR)
0,38
0,2
0,8
Power ICA
Graph Power ICA
0,2
0,8
MSE
MD

## Slide 49: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)
Input signals
Graph Power ICA
Power ICA

## Slide 50: Graph BSS Results Outlier contamination
Breakdown point already with one large outlier (100std)
0,8
0,4
0,4
1,4
MSE
MD
1,0
Power ICA
Graph Power ICA

## Slide 51: Towards EEG data Synthetic EEG artifact reconstruction
Semi-synthetic EEG data:
3. We generated realistic artifacts and added one on each channel
Artifacts which typically come along with EEG data [Delorme2006]
Optional: Add single or patchy (1000std) Outliers and white noise (3std)
1. Use real EEG data as input signals
2. Mix Data with random mixing matrix
4. Perform Power ICA and Graph Power ICA
EEG data:
Muscle
Eye Blink
Electrical
Electrical
Synthetic EEG artifacts:
Notes: Show reconstructed artifacts

## Slide 52: Graph BSS Results Semi-synthetic EEG data
Muscle
Eye Blink
Electrical
Electrical
Noise
0
1
2
3
4
5
6
0
1
2
3
4
5
6
t[s]
t[s]
Artifacts clearly extractable:
Power ICA
EEG artifacts

## Slide 53: Graph BSS Results Semi-synthetic EEG data
Also possible with Graph Power ICA:
0
1
2
3
4
5
6
t[s]
Graph Power ICA
0
1
2
3
4
5
6
t[s]
Power ICA

## Slide 54: Graph BSS Results Semi-synthetic EEG data
Events clearly extractable:
Button push
Visual stimulus
Power ICA
0
1
2
3
4
5
6
t[s]

## Slide 55: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 56: Summary of major outcomes
Question 1: What is ICA?
Question 2: How to compare algorithms?
Question 3: Which algorithm performs best? What happens with noise or outlier?
Question 4: How to robustify algorithms?
Question 5: What is Graph Signal processing / Graph BSS?
Question 6: Outcomes of Graph Signal processing?

## Slide 57: Summary of major outcomes Question 1: What is ICA?
  Mathematical concept to extract (independent = non-gaussian) signals from mixed signals
  Different approaches to obtain the demixing matrix  4 algorithms
  „ICA tries to decorrelate mixed up signals and find the optimal demixing matrix based on optimizing different measures of independence“
CoroICA

## Slide 58: Summary of major outcomes Question 2: How to compare algorithms?
  Minimum distance, MSE and SNR
  Correlation of different metrics important
  „One Metric sometimes provides not the whole information: We need to find how different metrics correlate“
0,0
0,8
0,2
0,4
0,6
0,0
0,8
0,2
0,4
0,6
1,0
Median of MSEs
Minimum Distance
0,4
0,19
0,1
0,6
Power ICA
Graph Power ICA
MD

## Slide 59: Summary of major outcomes Question 3: Which algorithm performs best? What happens with noise or outlier?
  Monte Carlo run with 10.000 runs: Evaluate metrics
    More or less similar with good data (simulated and real EEG data with added artifacts)
    Power ICA: quite good with reasonable SNR (~ 20dB), fast and with low variance
    Low sample sizes are problematic (< 5000 samples)
    Higher noise than 20dB SNR: smoothly becoming worse
    All reach breakdown point with one large outlier
  „All four algorithms: Good performance on well behaving data but higher noise level or larger outlier cause
  failure  Violates assumptions“
Notes: Low sample size problematisch: central limit theorem  finite variance (ausreißer macht infinite variance)
Gaussian noise (gegen die Annnahmen von ICA)
Ergebnisse machen Sinn: Annahmen über ICA
Robustness nicht gegeben, da asymptotisches Verhalten verändert
Assumptions sagen!
iid, finite covariance, dürfen nicht Gauss sein

## Slide 60: Summary of major outcomes Question 4: How to robustify?
  Whitening process crucial for algorithms
  Different objective functions for some algorithms
  Initialization quite important (local maxima/minima)
  Within algorithms: quite complicated  model based
  What we tried:
    Plug-in robustness of covariance estimation in whitening process
    Trying out different robust objective functions
    Initialize Power ICA with Radical as a global optimizer
  „No real improvement: sometimes with noise a bit better, but still low
  breakdown point”
Notes: Robust whitening: probem mit outlier
Problem mit outlier: Unterschied non-Gaussian signals und non-Gaussian outlier
Annahmen verletzen -> ist sinnvoll das es nicht funktioniert
=> Model gibt es nícht her

## Slide 61: Summary of major outcomes Question 5: What are Graph Signals / Graph BSS?
  Graph signal: Use proximity/similarity between components of the underlying signal
  „Graph BSS tries to combine the ICA approach to maximize the measure of independence and the graph signal approach to decorrelate the nodes of the graph”
1
N
0
2
3
…
Notes: - Wir haben uns damit beschäftigt!

## Slide 62: Summary of major outcomes Question 6: Outcomes of Graph BSS?
  Monte Carlo with 1000 runs:
    Better Blind Source Separation with good signals (low sample size)
    Similar with noisy data
    Breakdown point with one outlier as well
    Problem with graph structure
„Graph BSS is good for low sample sizes and if the graph structure is available. Otherwise similar outcomes as standard BSS”
Real EEG data with artifacts separable!
Notes: - ICA vesagt: also versagt auch Graph BSS

## Slide 63: Agenda
Understanding the basis of Source Separation via an intuitive example-driven approach
Discussion of experiment design
Graph Blind Source Separation
Graph Blind Source Separation results
Summary of major outcomes
Problems and future research

## Slide 64: Problems and future research
Problems:
Low Breakdown point
High noise dependency
Sample size important for standard ICA
Graph structure estimation: How to find correlation of graph signals?
Covariance estimation in higher dimensions problematic
Time consumption for real time EEG analysis
Future research:
Robust whitening / preprocessing (Robust covariance estimation in high dimensions)
Incorporate noise process and outlier in model for ICA algorithm
Find good graph structure estimation (recent research [Garcia2020])
Notes: Defusion based vs decorrelation based (-> time and spatial )
- New Outlier & non-Gaussianity measure finden

## Slide 65: Thank you for your attention!

## Slide 66: Literature Chapter 1
[NY Times, 2020] https://www.nytimes.com/2018/01/18/arts/design/brain-neuroscience-santiago-ramon-y-cajal-grey-gallery.html
[BackyardBrains] https://backyardbrains.com/experiments/EEG#prettyPhoto
[iStock] https://medium.com/better-humans/how-to-have-more-meaningful-conversations-7b1f9120ff0d
[Hyvärinen, 1999] "Fast and robust fixed-point algorithm for independent component analysis" IEEE Trans. Neural Netw. vol. 10 no. 3 pp. 626-634 May 1999.
[Basiri, 2017] S., Ollila, E., & Koivunen, V. (2017). Alternative Derivation of FastICA with Novel Power Iteration Algorithm. IEEE Signal Processing Letters, 24(9), 1378-1382. [7994645]. https://doi.org/10.1109/LSP.2017.2732342
[Jutten, 2010] Handbook of Blind Source Separation: Independent Component Analysis and Applications
[Shlens, 2010]: A Tutorial on Independent Component Analysis
[Haykin, 2009], Neural Networks and Learning Machines
[Sejnowski TJ , 1995] Bell AJ, Sejnowski TJ (November 1995). "An information-maximization approach to blind separation and blind deconvolutio
[Learned-Miller, 2003] John W. Fisher III, "ICA Using Spacings Estimates of Entropy", Journal of Machine Learning Research 4 (2003) 1271-1295
[Pfister 2019], Robustifying Independent Component Analysis by Adjusting for Group-Wise Stationary Noise, Sebastian Weichwald, Peter Bühlmann, Bernhard Schölkopf; 20(147):1−50, 2019.
[Belouchrani 1997], K. Abed-Meraim, J.-F. Cardoso, and E. Moulines, “A Blind Source Separation Technique Using Second-Order Statistics,” IEEE Transactions on Signal Processing, vol. 45, no. 2, pp. 434–444, 1997.
[Cardoso 1993 ], A. Souloumiac, “Blind Beamforming for non Gaussian Signals,” IEEE Proceedings-F, vol. 140, pp. 362–370, 1993.

## Slide 67: Literature Chapter 2
[Miettinen, 2020] Graph Signal Processing Meets Blind Source Separation, Jari Miettinen, Esa Ollila et al., 2020
[Blöchl, 2010] Second-Order Source Separation Based on Prior Knowledge Realized in a Graph Model, Florian Blöchl, Andreas Kowarsch, Fabian J. Theis, 2010
[Djuric, 2018] Cooperative and Graph Signal Processing Principles and Applications, Petar Djuric, Cédric Richard, 2018

## Slide 68: Literature Chapter 3
[Delorme2007] - Enhanced detection of artifacts in EEG data using higher-order statistics and independent component analysis in NIH 2007
[Koudelková2018] - Introduction to the identification of brain waves based on their frequency

## Slide 69: Literature Chapter 3
Delorme et al.: “Enhanced detection of artifacts in EEG data using higher-order statistics and independent component analysis”, Elsevier 2006
Garcia et al.: ”Blind Demixing of Diffused Graph Signals”, arXiv 2020

## Slide 70: Back Up I: Alternative Interpretation of ICA
What is the goal of the algorithm?
Find the demixing matrix so that the latent source variable s can be reconstructed as by the observed data
How can the the Independent Components be interpreted?
Amplitudes recorded simultaneously in microphones 1 and 2 are plotted on the x and y axes for each sound (waterfall, student) separately
Waterfall: samples lie on the vector reflecting the proximity of the sound to microphones 1 and 2
Independent components represent to the basis used to generate the data
Notes: The goal if ICA is to solve BSS problems which arise from a linear mixture
Find two unknowns A and s by only obersving theier matrix product x, underconstrained problem,
Amplitudes
Unsupervised learning problem

## Slide 71: Back Up II: Notes on peculiarities of ICA
Original Signals
Reconstructred signal Signals
Due to ambiguities of the method the extracting of the unobserved independent source signals is only accurate up to:
𝑑 × 𝑑 permutation matrix , scaling matrix and sign-change matrix
Permutation
Permutation
Sign Change
Scaling
Notes: P = (obtained by permuting the rows of 𝑑 × 𝑑 identity matrix),
D = (a diagonal matrix with positive diagonal elements)

## Slide 72: Back Up III: Towards EEG data Results with synthetic EEG data
Mixed signals + added artifacts
Reconstructed signals + artifacts
PowerICA
Able to reconstruct the standard signals and the EEG artifacts
Eye Blink
Muscle
electrical
electrical

## Slide 73: Back Up IV: Distribution of Signals
clean
mixed
whitened
demixed