## Slide 1: Agenda
1. Understanding the Basis of Source Separation via an Intuitive Example-Driven
Approach
2. Discussion of Experiment Design
3. Graph Blind Source Separation
4. Graph Blind Source Separation results
  Summary of major outcomes
  Problems and future research

## Slide 2: Shortcomings
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one Gaussian signal
For SNR ≤ 20dB high variance in performance
    Failures become increasingly likely
Inherently unrobust against outliers
    A single outlier will lead to failure of the method
3. SNR ≤ 20dB
2. Gaussian
4. Outlier
1. Samples
N

## Slide 3: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory [1]
In 2020: First approaches to combine non-Gaussianity based BSS with graph based BSS (Jari Miettinen et al.) [2]
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)

## Slide 4: Recent Developments
In 2010: Blind Source Separation(BSS) using graph theory [1]
In 2020: First approaches to combine non-Gaussianity based BSS with graph based BSS (Jari Miettinen et al.) [2]
What is the idea?
Design a method that uses:
  Non-Gaussianity measure (classic ICA)
  Information about underlying graph structure
Combine those in a way that they complement each other

## Slide 5: Graph Blind Source Separation What are Graphs?

## Slide 6: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
Edges represent proximity between two vertices
Graph structure can be stored in a matrix ⇒ The adjacency matrix A
Examples: Social networks, sensor networks, brain networks, etc. [3]
7
2
5
4
6
1
3
Undirected unweighted graph
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
A =

## Slide 7: Graph Blind Source Separation What are Graphs?
Graphs are structures build by vertices that are connected by edges
Edges represent proximity between two vertices
Graph structure can be stored in a matrix ⇒ The adjacency matrix A
Examples: Social networks, sensor networks, brain networks, etc. [3]
7
2
5
4
6
1
3
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
1 0 0 0 0 0 0
A =
Undirected unweighted graph

## Slide 8: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Each node represents a sample point
Directed graph ⇒ unsymmetric adjacency [3]
1
N
0
2
3
…
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
A =
1 0 0 0 0 0 … 0
. . . . . . … 0
n ∈ ℕ, n ≤ N

## Slide 9: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
Multiple Signals can share the same graph
In this case: The class of all periodic signals with period N [3]
0 1 0 0 0 0 … 0
0 0 1 0 0 0 … 0
0 0 0 1 0 0 … 0
0 0 0 0 1 0 … 0
. . . . . . … 1
A =
1 0 0 0 0 0 … 0
. . . . . . … 0
1
N
0
2
3
…
n ∈ ℕ, n ≤ N

## Slide 10: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
We call a graph shift by k
  For Line Graph ⇔ Shift operator as known from Digital Signal Processing
When a graph shift is applied, the signal will shift along every connected path made up of the k nearest edges. [3]
1
N
0
2
3
…
n ∈ ℕ, n ≤ N
k = 1 shift

## Slide 11: Graph Blind Source Separation What are Graph Signals?
Analogy to discrete time signals
Simplest case: Recursive Line Graph
We call a graph shift by k
  For Line Graph ⇔ Shift operator as known from Digital Signal Processing
When a graph shift is applied, the signal will shift along every connected path made up of the k nearest edges. [3]
1
N
0
2
3
…
n ∈ ℕ, n ≤ N
k = 1 shift

## Slide 12: Graph Blind Source Separation Graph Autocorrelation
Using the introduced graph shift we define the graph autocorrelation matrix analog to the sample autocorrelation [1] :
D dimensional square matrix of sample autocorrelation
D dimensional square matrix of graph autocorrelation for k graph-shifts
k-th power of adjacency matrix corresponding to k shifts along the graph
D signals stored as column vectors
The k-shift along paths of an underlying graph can provide additional information about independence between signals!
,
: Identity Matrix

## Slide 13: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
Find a matrix that diagonalizes as much as possible [1]
The solution for decorrelates the signals in the graph-sense
  is a solution of the BSS problem for graph-signals
N

## Slide 14: Graph Blind Source Seperation Graph Decorrelation
Advantages | Disadvantages
Independent of data distribution | Graph structure not directly available
Works well with small sample sizes | Highly dependent on accurate graph
Graph structure in many real- world problems | 
N
PowerICA shortcomings:
Significant performance loss for sample sizes with N << 5000
Unable to recover more than one Gaussian signal
Graph based BSS and non-Gaussianity based BSS seem to make up for each others weak points.

## Slide 15: Graph Blind Source Seperation Composite Objective
Composite objective function
How can we combine them?
Approach from Jari Miettinen et al. (Aalto University) [2]
Define composite objective function :
PowerICA objective:
Maximize estimate of non-Gaussianity with the Lagrangian method.
Graph decorrelation objective:
Diagonalize graph autocorrelation matrix(matrices) as much as possible. For only one adjacency ⇒ eigenvalue problem.
+
Balance Parameter

## Slide 16: Literature
[1] Graph Signal Processing Meets Blind Source Separation, Jari Miettinen, Esa Ollila et al., 2020
[2] Second-Order Source Separation Based on Prior Knowledge Realized in a Graph Model, Florian Blöchl, Andreas Kowarsch, Fabian J. Theis, 2010
[3] Cooperative and Graph Signal Processing Principles and Applications, Petar Djuric, Cédric Richard, 2018